## Slide 1: WAVELET TRANSFORM
Supervisor: Dr. Lý Quốc Ngọc
Group 9: Hồ Quang Minh - 1211042
Đỗ Đặng Minh - 1311015
Huỳnh Công Toàn - 1311026
Dương Xuân Long - 1311048
Hồ Văn Tấn - 1311058
Notes: Version: 1.0
Last update: September 25, 2014

## Slide 2: OUTLINE
Fourier Transform
Wavelet Transform
  Continuous Wavelet Transform
  Multiresolution Analysis
  Discreet Wavelet Transform
  2D Wavelet Transform
  Fast Wavelet Transform
  Wavelet Packet
Wavelet Transform Application
Demo

## Slide 3: FOURIER TRANSFORM
Frequency domain: Joseph Fourier (1807).
Cannot provide simultaneously time and frequency information.
Notes: Transform: A mathematical operation that takes a function or sequence and maps it into another one
The transform of a function may give additional /hidden information about the original function, which may not be available/obvious otherwise
The transform of an equation may be easier to solve than the original equation
The transform of a function/sequence may require less storage, hence provide data compression / reduction
An operation may be easier to apply on the transformed function, rather than the original function (recall convolution)

## Slide 4: FOURIER TRANSFORM
Recall that FT uses complex exponentials (sinusoids) as building blocks.
For each frequency of complex exponential, the sinusoid at that frequency is compared to the signal.
If the signal consists of that frequency, the correlation is high  large FT coefficients.
If the signal does not have any spectral component at a frequency, the correlation at that frequency is low / zero,  small / zero FT coefficient.

## Slide 5: Stationary and Non-stationary Signals
FT identifies all spectral components present in the signal, however it does not provide any information regarding the temporal (time) localization of these components. Why?
Stationary signals consist of spectral components that do not change in time
  all spectral components exist at all times
  no need to know any time information
  FT works well for stationary signals
However, non-stationary signals consists of time varying spectral components
  How do we find out which spectral component appears when?
  FT only provides what spectral components exist , not where in time they are located.
  Need some other ways to determine time localization of spectral components

## Slide 6: Stationary and Non-stationary Signals
Stationary signals’ spectral characteristics do not change with time
Non-stationary signals have time varying spectra
Concatenation

## Slide 7: SHORT-TIME FOURIER TRANSFORM
Time-Frequency analysis: STFT (Dennis Gabor 1946).
Time
parameter
Frequency
parameter
Signal to
be analyzed
FT Kernel
(basis function)
STFT of signal x(t):
Computed for each
window centered at t=t’
Windowing
function
Windowing function
centered at t=t’
Notes: Choose a window function of finite length
Put the window on top of the signal at t=0
Truncate the signal using this window
Compute the FT of the truncated signal, save.
Slide the window to the right by a small amount
Go to step 3, until window reaches the end of the signal
For each time location where the window is centered, we obtain a different FT
  Hence, each FT provides the spectral information of a separate time-slice of the signal, providing simultaneous time and frequency information

## Slide 8: SHORT-TIME FOURIER TRANSFORM
Wide analysis window  poor time resolution, good frequency resolution.
Narrow analysis window  good time resolution, poor frequency resolution
Once the window is chosen, the resolution is set for both time and frequency.
Notes: Choose a window function of finite length
Put the window on top of the signal at t=0
Truncate the signal using this window
Compute the FT of the truncated signal, save.
Slide the window to the right by a small amount
Go to step 3, until window reaches the end of the signal
For each time location where the window is centered, we obtain a different FT
  Hence, each FT provides the spectral information of a separate time-slice of the signal, providing simultaneous time and frequency information

## Slide 9: Heisenberg Uncertainty Principle
Time resolution: How well two spikes in time can be separated from each other in the transform domain
Frequency resolution: How well two spectral components can be separated from each other in the transform domain
Both time and frequency resolutions cannot be arbitrarily high!!!  We cannot precisely know at what time instance a frequency component is located. We can only know what interval of frequencies are present in which time intervals

## Slide 10: WAVELET TRANSFORM
Decomposition of a signal into constituent parts.
Notes: Fourier series: harmonic sinusoids; single integer index
Fourier transform (FT): nonharmonic sinusoids; single real index
Walsh decomposition: “harmonic” square waves; single integer index
Karhunen-Loeve decomp: eigenfunctions of covariance; single real index
Short-Time FT (STFT): windowed, nonharmonic sinusoids; double index
Wavelet Transform: time-compacted waves; double index

## Slide 11: WAVELET TRANSFORM
Overcomes the preset resolution problem of the STFT by using a variable length window
Analysis windows of different lengths are used for different frequencies:
  Analysis of high frequencies Use narrower windows for better time resolution
  Analysis of low frequencies  Use wider windows for better frequency resolution
This works well, if the signal to be analyzed mainly consists of slowly varying characteristics with occasional short high frequency bursts.
Heisenberg principle still holds!!!
The function used to window the signal is called the wavelet

## Slide 12: WAVELET TRANSFORM
Wavelet transform also provides time-frequency view
  Decomposes signal in terms of duration-limited, band-pass components
    high-frequency components are short-duration, wide-band
    low-frequency components are longer-duration, narrow-band
  Can provide combo of good time-frequency localization and orthogonality
    the STFT can’t do this
  More precisely, wavelets give time-scale viewpoint
    this is connected to the multi-resolution viewpoint of wavelets

## Slide 13: TYPES OF WAVELET
Daubechies
Mexican hat
Morlet
Shannon
Haar

## Slide 14: TYPES OF WAVELET
Haar wavelet:
  Wavelet function
  Scaling function

## Slide 15: Image Pyramids
Compute a reduced-resolution approximation of the input image
  Filtering (Averaging, Gaussian)
  Down-sampling
Up-sample the output of the previous by a factor 2
Compute the difference between the prediction of step 2 and the input to Step 1.

## Slide 16: Image Pyramids

## Slide 17: MULTIRESOLUTION ANALYSIS
In Multi-resolution Analysis (MRA), a Scaling Function is used to create a series of approximations of a function or image, each differing by a factor 2 from its nearest neighboring approximations. Additional functions, called Wavelet, are used to encode the difference in information between adjacent approximation.

## Slide 18: MULTIRESOLUTION ANALYSIS
Idea: If a set of signals can be represented by a weighted sum of φ(t-k), a larger set (including the original), can be represented by a weighted sum of φ (2t-k).
Subspace: .
Increase the size of the subspace changing the time scale of the scaling functions:
Real-valued expansion coefficients
Real-valued expansion functions

## Slide 19: MULTIRESOLUTION ANALYSIS
The spanned spaces are nested:
Wavelets span the differences between spaces wi.
Wavelets and scaling functions should be orthogonal: simple calculation of coefficients.
Nested function spaces spanned by a scaling function

## Slide 20: WAVELET TRANSFORM - EXAMPLE
Suppose we are given the following input sequence.
{xn,i} = {10, 13, 25, 26, 29, 21, 7, 15}
Consider the transform that replaces the original sequence with its pairwise average xn−1,i and difference dn−1,i defined as follows:

## Slide 21: WAVELET TRANSFORM - EXAMPLE
10 | 13 | 25 | 26 | 29 | 21 | 7 | 15
11.5 | 25.5 | 25 | 11 | -1.5 | -0.5 | 4 | -4
18.5 | 18 | -7 | 7 | -1.5 | -0.5 | 4 | -4
18.25 | 0.25 | -7 | 7 | -1.5 | -0.5 | 4 | -4
{10, 13, 25, 26, 29, 21, 7, 15}

## Slide 22: WAVELET TRANSFORM - EXAMPLE
The averages and differences are applied only on consecutive pairs of input sequences whose first element has an even index.
The number of elements in each set {xn−1,i} and {dn−1,i} is exactly half of the number of elements in the original sequence.
Form a new sequence having length equal to that of the original sequence by concatenating the two sequences {xn−1,i } and {dn−1,i}. The resulting sequence is
{xn,i, dn-1,i} = {11.5, 25.5, 25, 11, −1.5, −0.5, 4, −4}

## Slide 23: WAVELET TRANSFORM - EXAMPLE
This sequence has exactly the same number of elements as the input sequence - the transform did not increase the amount of data.
Since the first half of the above sequence contain averages from the original sequence, we can view it as a coarser approximation to the original signal.
The second half of this sequence can be viewed as the details or approximation errors of the first half.

## Slide 24: WAVELET TRANSFORM - EXAMPLE
Synthesis: The original sequence can be reconstructed from the transformed sequence using the relations
Analysis (Haar wavelet transform)

## Slide 25: WAVELET TRANSFORM - EXAMPLE
10 | 13 | 25 | 26 | 29 | 21 | 7 | 15
11.5 | 25.5 | 25 | 11 | -1.5 | -0.5 | 4 | -4
18.5 | 18 | -7 | 7 | -1.5 | -0.5 | 4 | -4
18.25 | 0.25 | -7 | 7 | -1.5 | -0.5 | 4 | -4
{18.25, 0.25, -7, 7, -1.5, -0.5, 4, 4}

## Slide 26: WAVELET TRANSFORM - EXAMPLE
Input image for the 2D Haar Wavelet Transform.
(a) The pixel values. (b) Shown as an 8×8 image.

## Slide 27: WAVELET TRANSFORM - EXAMPLE
Intermediate output of the 2D Haar Wavelet Transform.

## Slide 28: WAVELET TRANSFORM - EXAMPLE
Output of the first level of the 2D Haar Wavelet Transform.

## Slide 29: CONTINUOUS WAVELET TRANSFORM
Width of the window is changed as the transform is computed for every spectral components.
: translation (The location of the window)
: scale
: mother wavelet

## Slide 30: CONTINUOUS WAVELET TRANSFORM
Wavelet function:
or
Invert CWT:
Continuous transform: map functions to functions
Discrete transform: map sequences to sequences

## Slide 31: CONTINUOUS WAVELET TRANSFORM
From http://www.cerm.unifi.it/EUcourse2001/Gunther_lecturenotes.pdf, p.10
Lát cắt tần số-thời gian của Biến đổi Fourier và biến đổi wavelet

## Slide 32: DISCREET WAVELET TRANSFORM
Using Multiresolution Analysis.
: scaling function
: wavelet function
Invert DWT:

## Slide 33: DISCREET WAVELET TRANSFORM
DWT filter bank
g[n]: lowpass filter, scaling function
h[n]: highpass filter, wavelet function
downsampling

## Slide 34: DISCREET WAVELET TRANSFORM
Wavelet transforms
  Low pass filtering: averaging
  High pass filtering: differencing
  Input data: a, b
  Average: s = (a + b) / 2 (low pass filtering)
  Difference: d = a – s (high pass filtering)
  Wavelet coefficients: (s, d).
Inverse wavelet transforms: addition; subtraction
  Wavelet coefficients: (s, d).
  Addition: s + d = s + (a – s) = a,
  Subtraction: s – d = s – (a – s) = 2s – a = b
  Input data: (a, b).

## Slide 35: DISCREET WAVELET TRANSFORM
Example: input data 14, 22
  Wavelet Transform
Average: s = (14＋22)/2 = 18,
Difference: d = 14-18= -4
Wavelet coefficients: (18, -4).
  Inverse Wavelet Transform (to recover the input data)
s ＋ d = 18+(-4) = 14,
s － d = 18-(-4) = 22
Input data: (14, 22).

## Slide 36: DISCREET WAVELET TRANSFORM

## Slide 37: 2D Wavelet Transform
For an N by N input image, the two-dimensional DWT proceeds as follows:
  Convolve each row of the image with h0[n] and h1[n], discard the odd numbered columns of the resulting arrays, and concatenate them to form a transformed row.
  After all rows have been transformed, convolve each column of the result with h0[n] and h1[n]. Again discard the odd numbered rows and concatenate the result.

## Slide 38: 2D Wavelet Transform
After the above two steps, one stage (level) of the DWT is complete.
The transformed image now contains four subbands
LL, HL, LH, and HH, standing for low-low, high-low, etc.
The LL subband can be further decomposed to yield yet another level of decomposition.
This process can be continued until the desired number of decomposition levels is reached.

## Slide 39: 2D Wavelet Transform
The two-dimensional discrete wavelet transform
(a) One level transform. (b) Two level transform.

## Slide 40: FAST WAVELET TRANSFORM
Basic idea of Fast Wavelet Transform
(Mallat’s herringbone algorithm):
  Pyramid algorithm provides an efficient calculation.
  DWT (direct and inverse) can be thought of as a filtering process.
  After filtering, half of the samples can be eliminated: subsample the signal by two.
    Subsampling: Scale is doubled.
    Filtering: Resolution is halved.

## Slide 41: FAST WAVELET TRANSFORM
Decomposition:

## Slide 42: FAST WAVELET TRANSFORM
Decomposition:

## Slide 43: FAST WAVELET TRANSFORM
Decomposition:

## Slide 44: FAST WAVELET TRANSFORM
Decomposition:

## Slide 45: FAST WAVELET TRANSFORM
Synthesis

## Slide 46: FAST WAVELET TRANSFORM
Synthesis

## Slide 47: FAST WAVELET TRANSFORM

## Slide 48: FAST WAVELET TRANSFORM

## Slide 49: LIFTING SCHEME
The lifting scheme is an alternative method of computing the wavelet coefficients.
Advantages of the lifting scheme:
  Requires less computation and less memory.
  Linear, nonlinear, and adaptive wavelet transform is feasible, and the resulting transform is invertible and reversible.

## Slide 50: LIFTING SCHEME
A spatial domain construction of bi-orthogonal wavelets, consists of the 4 operations:
  Split : sk(0)=x2i(0), dk(0)=x2i+1(0)
  Predict : dk(r)= dk(r-1) – pj(r) sk+j(r-1)
  Update : sk(r)= sk(r-1) + uj(r) dk+j(r)
  Scaling : sk(R)=K0sk(R), dk(R)=K1dk(R)

## Slide 51: LIFTING SCHEME
A spatial domain construction of bi-orthogonal wavelets, consists of the 4 operations:

## Slide 52: LIFTING SCHEME
Example: Conventional 5/3 filter
    C0 = (4*x[0]+2*x[0]+2*(x[-1]+x[1])-(x[2]+x[-2]) )/8
    C1 = x[0]- (x[1]+x[-1])/2
    Number of operations per pixel = 9+3 = 12

## Slide 53: WAVELET PACKET
In the usual dyadic wavelet decomposition (transform), only the low-pass filtered subband is recursively decomposed and thus can be represented by a logarithmic tree structure.
A wavelet packet decomposition allows the decomposition to be represented by any pruned subtree of the full tree topology.
The wavelet packet decomposition is very flexible.
The computational requirement for wavelet packet decomposition is relatively low as each decomposition can be computed in the order of N logN using fast filter banks.

## Slide 54: WAVELET TRANSFORM APPLICATION
Compress image: JPEG 2000
Compress video
Compress speech/audio
Store digital Fingerprints
Fingerprints authentication
Reduce noise
Edge detection
…

## Slide 55: DEMO
Haar wavelet transform
  Compress image
  Reduce noise
  Wavelet transform on depth image
  Wavelet transform on RGD-D image

## Slide 56: REFERENCE
English:
  M. Sifuzzaman, M.R. Islam, M.Z. Ali: “Application of Wavelet Transform and its Advantages Compared to Fourier Transform”, Vidyasagar University, 2009.
  Rafael C. Gonzalez & R. E. Woods: “Digital Image Processing Third Edition”, Prentice Hall, ISBN 978-0131687288, pp. 483-543, 2006.
  Richard Szeliski: “Computer Vision: Algorithms and Applications”, Springer, ISBN 978-1848829343, pp. 154-160, 2010.
Vietnamese:
  Đỗ Ngọc Anh: “Nén ảnh sử dụng biến đổi wavelet và ứng dụng trong các dịch vụ dữ liệu đa phương tiện di động”, Đại học Bách Khoa Hà Nội, 2006.
  Nguyễn Thị Lụa: “Nghiên cứu lý thuyết wavelet trong xử lý tín hiệu”, Đại học Bách Khoa Hà Nội, 2001.
  Trần Duy Hưng: “Kỹ thuật xử lý ảnh sử dụng biến đổi Wavelet”.
Website:
  http://en.wikipedia.org/wiki/Wavelet_transform
  http://www.mathworks.com/help/wavelet/ug/wavelet-packets.html